## Slide 1: Autonomous Car Course Lane Detection Pipeline
Project Theory and Architecture Presentation
10-12 Slides Overview

## Slide 2: The Perception Problem in Autonomous Driving
Autonomous vehicles must perceive road geometry to navigate safely.
  Challenges in Lane Detection:
    Dynamic lighting and deep shadows
    Faded or missing road markings
    Occlusions from other vehicles
  Our solution: A robust, multi-stage classical computer vision pipeline.

## Slide 3: Pipeline Architecture Overview
The end-to-end processing steps:
  1. Color & Gradient Feature Extraction
  2. Region of Interest (ROI) Masking
  3. Perspective Transform (Bird's Eye View)
  4. Hough Transform & Histogram Peak Detection
  5. Sliding Window Poly-Fitting
  6. Temporal Smoothing & Curvature Math

## Slide 4: Color Space & Contrast Enhancement
Moving away from RGB limitations:
  HLS Color Space: Separates lightness from color information, highly invariant to shadows.
  Saturation (S) Channel: Excellent for tracking yellow and white lines.
  CLAHE Application: Contrast Limited Adaptive Histogram Equalization boosts local contrast in shadowed regions without blowing out highlights.

## Slide 5: Gradient & Edge Detection
Extracting structural boundaries:
  Gaussian Blur: Eliminates high-frequency noise.
  Sobel-X Operator: Detects steep intensity gradients in the x-direction (vertical lines).
  Canny Edge Detector: Computes edges using dynamic hysteresis thresholding based on local median pixel intensity.
  The resulting binary map fuses color and gradient evidence.

## Slide 6: Perspective Transform (Bird's-Eye View)
Removing perspective distortion:
  A homography matrix (M) maps a trapezoidal ROI in the camera view to a rectangle.
  Benefits of top-down projection:
    Parallel lane lines actually appear parallel.
    Enables accurate polynomial fitting.
    Allows uniform pixel-to-meter scaling for curvature calculation.

## Slide 7: Hough Transform & Base Selection
Finding the starting points of the lanes:
  Probabilistic Hough Transform extracts line segments from the binary edges.
  Column-wise Histogram aggregates white pixel density along the bottom half of the image.
  The algorithm cross-references histogram peaks with Hough segment intercepts to select the true left and right lane bases.

## Slide 8: Sliding Window Search
Tracing the lane up the image:
  Divides the image into 12 horizontal bands.
  Places rectangular windows at the left and right bases.
  Calculates the center of mass of non-zero pixels inside the window.
  Shifts the window for the next horizontal band to follow the curve of the lane.

## Slide 9: Polynomial Fitting & Outlier Rejection
Mathematical modeling of the lanes:
  Fits a 2nd degree polynomial: x = a*y^2 + b*y + c
  Statistical Outlier Rejection:
    Calculates residuals of all pixels against the initial fit.
    Discards pixels beyond the 75th percentile error limit.
    Refits the polynomial for a perfectly smooth curve.

## Slide 10: Missing Lane Inference
Handling dashed lines or heavy occlusions:
  If one side fails validation (e.g., hidden by a truck), the system infers its position.
  Takes the valid polynomial from the visible side.
  Shifts the 'c' intercept coefficient by the historically known lane width (approx. 3.7 meters).
  Maintains tracking safely until the line becomes visible again.

## Slide 11: Temporal Smoothing & Validation
Ensuring a fluid visual experience:
  Frame-by-frame processing is jittery.
  Deque History: Stores the N most recent polynomial coefficients.
  Final Render: A weighted average (low-pass filter) of the historical fits.
  Validates the left and right curves together to ensure they remain perfectly parallel.

## Slide 12: Conclusion & Output Rendering
Finalizing the pipeline:
  Calculates the physical Radius of Curvature using calculus on the polynomial equations.
  Draws the lane area in green and applies the Inverse Perspective Matrix (Minv) to unwarp it back to camera view.
  Alpha-blends the resulting graphics onto the original video feed for a cohesive autonomous driving visualization.